## Slide 1: Machine Learning Approach for Precise Localization of Wireless Nodes in Unmanned Aerial Vehicle Assisted Wireless Networks
Mr. Neerukattu Malyadri Naidu
Mr. Kondeti Venkata Kiran
Mr. Kodathala Anish Kumar Reddy
B. Tech ECE,
School of Electronics Engineering,
Under Guidance of:
Dr. Kalapraveen Bagadi,
Professor,
School of Electronics Engineering (SENSE)
Dr. Satyakumar V.,
R&D Mentor,
Notes: CV Presentation on

## Slide 2: Flow of Presentation
    Introduction
        Motivation
        Need of UAV Based Localization
        Research Objective
        Literature Review
    System Model For Node Localization
    Conclusions
      References
Notes: Optimization Based Least Square Localization (OLSL) Technique

## Slide 3: Introduction

## Slide 4
In the last 17 years, India has faced more than 300 natural disasters which resulted in 76,031 deaths in this millennium, according to the International Disaster Database (IDD).
The estimated damage sustained by India in the last 17 years due to these disasters amounts to USD 63.6 billion, according to the database.
This damage is mainly due to lack of proper surveillance.
Motivation
Figure 1: Disasters in different forms
Notes: Figure 1: Disasters in different forms

## Slide 5
Motivation Contd.
Figure 2: Applications of UAVs
Notes: Figure 1.2: Applications of UAVs

## Slide 6: Need of UAV Based Localization
The global positioning system (GPS) is a popular scheme that is used for outdoor localization, but it has several limitations.
Alternatively, few nodes can be selected as anchor nodes (ANs) and with the aid of these ANs, remaining nodes can determine their locations through localization process.
The localization with fixed terrestrial anchor nodes (FTANs) may fail when battles and disasters occur, where UAV assisted localization still works.
The implementation cost is much less as the only single UAV requires a GPS device.
Node localization using mobile aerial anchor (MAAN) deployed in UAVs provides high localization.

## Slide 7
To investigate efficient optimization techniques for optimizing least square localization problem.
To develop an accurate node localization algorithms even in highly nonlinear channel model.
Also to design localization techniques adaptable to mobile unknown nodes (UNs).
Finally, to achieve localization accuracy about (50–80) % better than the classical localization techniques.
Research Objectives

## Slide 8: Classification of Localization Techniques
GPS: Global Positional System
RSS: Received Signal Strength
TDoA: Time Difference of Arrival
ToA: Time of Arrival
AoA: Angle of Arrival
OTs: Optimization Techniques
ANN: Artificial Neural Networks
APIT: Approximate Point in Triangulation
Literature Review
Notes: GPS: Global Positional System

## Slide 9: Literature Review
Article | Journal and Year | Remarks
G. M. Djuknic, and R. E. Richton, “Geolocation and Assisted GPS” | IEEE Computer Magazine, 2001 | GPS based Localization using FTANs. Limited for indoor environment only
Li X, “Collaborative Localization with Received-Signal Strength in wireless sensor networks” | IEEE Trans. on Vehicular Tech., 2007 | RSSI based localization using FTANs. Limited by poor accuracy and high hardware complexity
L. Gui et. al., “Reference Anchor Selection and Global Optimized Solution for DV-Hop Localization in Wireless Sensor Networks ” | Wireless Personal Communications, 2017 | Range free localization using FTANs. Limited by very poor localization accuracy.
V. R. Kulkarni, V. Desai and R. V. Kulkarni, “A comparative investigation of deterministic and metaheuristic algorithms for node localization in wireless sensor networks” | Wireless Networks 2019 | Localization techniques using various OTs with FTANs. Provides trade-off between range free and range based localization techniques.
L. Zhao, X. Wen, D. Li, “Amorphous localization algorithm based on BP artificial neural network” | Inter. Journal of Dist. Sensor Net., 2015 | Provides better localization accuracy in FTAN based localization techniques.

## Slide 10: Literature Review Contd.
Article | Journal and Year | Remarks
S. K. Gharghan, R. Nordin, M. Ismail, J. A. Ali, “Accurate Wireless Sensor Localization Technique Based on Hybrid PSO-ANN Algorithm for Indoor and Outdoor Track Cycling” | IEEE Sensors Journal, 2016 | OTs and NN based Hybrid localization technique using FTAN. Provides better training for NNs.
Z. Gong, C. Li et. al., “Design, Analysis, and Field Testing of an Innovative Drone-Assisted Zero-Configuration Localization Framework for Wireless Sensor Networks” | IEEE Trans. on Veh. Tech. 2017 | Localization using multiple MAANs. Localization accuracy is better than FTANs
L. A. Villas, D. L. Guidoni et. al., “An energy efficient joint localization and synchronization solution for wireless sensor networks using unmanned aerial vehicle” | Wireless Networks, 2015 | Localization using single MAANs. Implementation complexity is fewer than localization using multiple MAANs
D. Popescu et. al., “A collaborative UAV-WSN network for monitoring large areas” | Sensors, 2018 | Localization using single MAANs.
S. Hazem, M. A. Mohammad, C. Alessandro, “Aerial Anchors Positioning for Reliable RSS-Based Outdoor Localization in Urban Environments” | IEEE Wire Comm Let., 2018 | RSSI based localization using multiple MAAN.

## Slide 11: System Model For Node Localization
Localization of Unknown Node Using Mobile Aerial Anchor Nodes

## Slide 12
Figure 4: Localization of Q target modes using P UAVs.

## Slide 13
Figure 5: Localization of qth target node using P AUs

## Slide 14: Localization of Unknown Node Using MAAN
The RSSI measurements recorded at the UN is based on the classic log normal shadow fading model (LNSM). The RSSI measured in dBm in the classical LNSM is given by:
then, the distance is estimated from:
where P0 is the RSS measured at reference distance d0
dpq is the true distance between qth UN and pth AN
γ is path loss exponent
χσ is the parameter representing log-normal shadow fading effects.
(1)
(2)
Notes: (01)

## Slide 15: Multilateration
The distances from all AN trajectory points to qth UN are given as:
The eq. (4) can be written in matrix form as:
U×Lq = V
where is the position of qth TN,
(3)
(4)

## Slide 16: Multilateration
Then, the location of qth TN can be obtained from:
(5)

## Slide 17
Highly nonlinear structures, the artificial neural network (ANN) models such as multilayer perceptron (MLP) and radial basis function (RBF) are effectively used for node localization under such nonlinear systems.
Another main advantage of ANN localization is that it supports mobility of UNs.
The MLP network is trained well using the popular back propagation (BP) algorithm and then the trained MLP network is used for node localization.
There exists feed forward connection among these, where information flows only in the forward direction, from inputs to outputs.
MLP Model for Node Localization

## Slide 18: Node Localization Using Multilayer Perceptron (MLP)

## Slide 19
Figure 10: Architecture of MLP model for localizing qth UN
UAV Assisted Node Localization Using MLP

## Slide 20
The neuron in the hidden layer consists of a summer and a nonlinear activation and hence the output of each hidden neuron is:
where, αhp denotes connection weight between the hth hidden node and pth input node.
The two output neurons are modelled with a simple summers. So, the estimated x, y and z positions of qth UN obtained from the two output neurons are described as:
Where, β1h , β2h and β3h are connection weights respectively from first, second and third output nodes to hth hidden node.
(6)
UAV Assisted Node Localization Using MLP Contd.
(7)

## Slide 21
Figure 10: Architecture of RNN model for localizing qth UN
UAV Assisted Node Localization Using RNN

## Slide 22
The RNN model shown in this figure has an input layer of P + 3 elements. Out of these P + 3 elements, P elements contains planar distances of qth TN from P AUs and 3 elements contains estimated x, y, and z position of the qth TN in the previous iteration that are feedback from output layer.
The output layer consists of three neurons and these neurons estimates x, y, and z position of the qth TN. the external input vector
and one time instant delayed output vector with zero initial state are combined to form an input vector a.
Hence, the kth element of the input vector is given by:
UAV Assisted Node Localization Using RNN Contd.
(8)

## Slide 23
Each output neuron consists of a summer and a non–linear activation. Hence, the estimated x, y and z coordinate of qth TN are obtained from the three output neurons as:
where, w1k, w2k and w3k respectively are the connection weights between first, second and third output nodes and kth input element.
The activation function ψ(.) is the same sigmoid activation function that we used for MLP.
UAV Assisted Node Localization Using RNN Contd.

## Slide 24: Simulation Analysis

## Slide 25
Table 1: Simulation Parameters
Parameter | Value
Sensor field dimension | (100×100×35) meters
Number of AUs (P) | 4
Number of TNs (Q) | 25
Height of the UAV (hp) | 40 meters
Height of the TNs (hq) | (0-35) meters
Path-loss constant (γ) | 3.1058
Standard deviation (σ) | 2.8189
Reference distance (d0) | 1 meter
Transmitted power at reference distance (P(d0)) | -27.143 dB
Number of output nodes of MLP and RNN | 3
Number of input nodes of MLP (P) | 4
Number of input nodes of RNN (P+3) | 7
Number of hidden neurons of the MLP (HN) | 8
Learning rate of MLP and RNN | 0.08
Notes: Table 1: Simulation Parameters

## Slide 26
Figure 5: Localization of qth TN using four AUs.

## Slide 27
(a) (b)
Notes: (a)

## Slide 28
(c)
Figure 6: RSS based localization of Q TNs with P AUs (a) P = 4 (b) P = 5 (c) P = 6
P | AvgLE (in meters)
4 | 4.1273
5 | 3.2424
6 | 2.8573
Table 2: ALE of RSS algorithm with increased number of AUs
Notes: (c)

## Slide 29
(a) (b)

## Slide 30
Figure 7: Localization of Q TNs with four AUs using (a) RSS (b) MLP (c) RNN
(c)
Technique | AvgLE (in meters)
RSS | 4.1273
MLP | 1.1035
RNN | 0.8462
Table 3: ALE of RSS algorithm with increased number of AUs

## Slide 31
(a) (b) (c)
Figure 8: Localization error computed for each TN while using: (a) RSS (b) MLP (c) RNN

## Slide 32: Conclusions
In this work, we have explored the concept of UAV-assisted node localization using neural networks in wireless sensor networks (WSNs).
The integration of UAVs and NN techniques offers a promising approach to address the challenges of accurate and efficient node localization.
The UAV-assisted node localization has several advantages for WSNs. It eliminates the need for manual calibration and configuration of sensor nodes, simplifying the deployment process.
Traditional localization technique in WSNs such as RSS often require manual configuration and suffer from limitations in accuracy, scalability, and efficiency.
However, the utilization of NNs, particularly MLP and RNN, allows for capturing complex spatial relationships and patterns, leading to improved localization accuracy.
Further, the RNN technique even performs better than MLP because RNN has a recurrent connection that allows it to maintain an internal memory.

## Slide 33: References
J. K. Sohraby, D. Minoli and T. Znati “Wireless Sensor Networks: Technology, Protocols, and Applications”, John Wiley & Sons Ltd, West Sussex, England, 1st edition, 2007.
A. Maddumabandara, H. Leung and M. Liu, “Experimental evaluation of indoor localization using wireless sensor networks”, IEEE Sens. J., vol. 15, pp. 5228–5237, 2015.
A. Khuwaja, Y. Chen, N Zhao N, Alouini M and P. Dobbins, “A Survey of Channel Modeling for UAV Communications”, IEEE Comm. Sur. & Tut., vol. 20, pp. 2804–2821, 2018.
F. Morbidi and G. L. Mariottini, “Active target tracking and cooperative localization for teams of aerial vehicles”, IEEE Trans. on Cont. Sys. Tech., vol. 21, pp. 1694–1707, 2013.
S. Subong, L. Bhoram and K. Jihoon, “Vision-based real-time target localization for single-antenna GPS-guided UAV”, IEEE Trans. on Aero. and Elect. Sys., vol. 44, pp. 1391–1401, 2008.
G. Han, J. Jiang, C. Zhang, T. Q. Duong, M. Guizani and G. K. Karagiannidis, “A Survey on Mobile Anchor Node Assisted Localization in Wireless Sensor Networks”, IEEE Comm. Sur. & Tut., vol. 18, pp. 2220–2243, 2016.

## Slide 34
R. Storn and K. V. Price, “Differential evolution-A simple and efficient heuristic for global optimization over continuous spaces”, J of Glob. Opt., vol. 11, pp. 341–359, 1997.
R. Harikrishnan, V. J. S. Kumar and P. S. Ponmalar, “A Comparative Analysis of Intelligent Algorithms for Localization in Wireless Sensor Networks”, Wire. Per. Comm., vol. 87, pp. 1057–1069, 2016.
S. Yun, J. Lee, W. Chung, E. Kim and S. Kim, “A soft computing approach to localization in wireless sensor networks”, Exp. Sys. with Appl., vol. 36, pp. 7552–7561, 2009.
J. Brest, S. Greiner, B. Boskovic, M. Mernik and V. Zumer, “Self-Adapting Control Parameters in Differential Evolution: A Comparative Study on Numerical Benchmark Problems”, IEEE Trans. on Evol. Comp., vol. 10, pp. 646–657, 2006.
D. Karaboga and B. Basturk, “powerful and efficient algorithm for numerical function optimization: Artificial bee colony (ABC) algorithm”, J. of Glob. Opt., vol. 39, pp. 459–471, 2007.
S. Kumar, R. Sharma and E. R. Vans, “Localization for Wireless Sensor Networks: A Neural Network Approach”, Int. J. of Comp. Net. & Comm., vol. 8, pp. 61–71, 2016.
G. B. Huang, Q. Y. Zhu and C. K Siew, “Extreme learning machine: Theory and applications”, Neurocomputing, vol. 70, pp. 489 – 501, 2006.

## Slide 35
G. M. Djuknic, and R. E. Richton, “Geolocation and Assisted GPS”, IEEE Comp. Mag., vol. 34, pp. 123-125, 2001.
Li X., “Collaborative Localization with Received-Signal Strength in wireless sensor networks”, IEEE Trans. on Veh. Tech., vol. 56, pp. 3807–3817, 2007.
L. Yang and K. C. Ho, “An Approximately Efficient TDOA Localization Algorithm in Closed Form for Locating Multiple Disjoint Sources with Erroneous Sensor Positions”, IEEE Trans. on Sig. Proc., vol. 57, pp. 4598–4615, 2009.
X. Enyang, Z. Ding, and S. Dasgupta, “Source Localization in Wireless Sensor Networks from Signal Time-of-Arrival Measurements” IEEE Trans. on Sig. Proc., vol. 59, pp. 2887–2897, 2011.
W. Zhang, Q. Yin, H. Chen, F. Gao, and Ansari, “Distributed Angle Estimation for Localization in Wireless Sensor Networks”, IEEE Trans. on Wire. Comm., vol. 12, pp. 527 – 537, 2013.
N. Bulusu, J. Heidemann, and D. Estrin, “GPS-less Low-Cost Outdoor Localization for Very Small Devices”, IEEE Per. Comm., vol. 7, pp. 28–34, 2000.
J. Bachrach, R. Nagpal, M. Salib, and H. Shrobe, “Experimental Results for and Theoretical Analysis of a Self-Organizing a Global Coordinate System from Ad Hoc Sensor Networks”, Telecomm. Sys., vol. 26, pp. 213 – 233, 2004.

## Slide 36: Thank You